## Slide 1: DANSS - detector of the reactor antineutrino (status report)
V.Egorov (DLNP JINR, Dubna)

## Slide 2
GEMMA experiment: search for the NMM
Since 2005 we do NMM measurements under the unit #2 of the KNPP – a standard 3GWth PWR (ВВЭР-1000)
Life-time ~ 320 days
1500 kg of 235U is burned out
and 311 kg of 239Pu is produced
which changes the flux and energy spectrum of the neutrino emitted
Would like to monitor the neutrino spectrum and flux (2.7∙1013 /cm2/s)

## Slide 3
For the monitoring we needed anything simple and reliable

## Slide 4: 20 years ago our colleagues from KI were the first who tried to perform the neutrino monitoring RONS (Rovno, UA) 1986-1990
Liquid scintillator (~1 m3)
in a special laboratory

## Slide 5
Days
Reactor operation after the fuel refilling
Counts per 100 000 sec
The group of
L.А. Mikhaelyan (КI):
Rovno NPP (UA) 1986-1990

## Slide 6
Neutrino energy [MeV]
Relative changes in the heutrino spectrum:
1 – Nν(actual) / Nν(initial)

## Slide 7: We want such detector!
«We» – means JINR (Dubna)
+
ITEP (Moscow)

## Slide 8: Which kind of detector ?
Generally ~1 m3 of liquid scintillator is used
RONS (SU), NUCIFER (FR), ANGRA (BR), SONGS1 (US), KASKA (JP)
 But: we have no experience in LS
 But: they say it is problematic (Gd…)
 But: is there any SANE DIRECTOR of NPP who allows to bring 1 ton of gasoline close to his reactor ?!
 How much better is plastic scintillator !..

## Slide 9: Detection idea: Inversed Beta-Decay

## Slide 10: Signature of the IBD registration
e+
(n,)
30-50 μs
(from 2.6)
to 8 MeV
Local burst
The burst
spread in space

## Slide 11: Detection of the reactor neutrino would allow:
Measure the actual reactor power (Nν)
Deduce the actual fuel composition (Eν)
Weak (ν-e) cross-section
On-line reactor monitoring (tomography?) – especially important in view of the future FBR (with longer life-time and less studied)
Non-proliferation (prevent unauthorized extraction of 239Pu)

## Slide 12
XY-view
# geometry of neutrino detector
# SCINTILLATOR BLOCKS
# in X axis
bottom-scinblock.number-of-columns=100
# in Y axis
bottom-scinblock.number-of-rows=25
# in X axis
bottom-scinblock.width=1 cm
# in Y axis
bottom-scinblock.length=4 cm
# in Z axis
bottom-scinblock.thickness=1 m
# material of capturer layer on the scintillator surface
# available materials: Gadolimium Cadmium
bottom-scinblock.n-capt.material=Cadmium
# thickness of capturer layer on the X surface
bottom-scinblock.n-capt.x-thickness = 150 micrometer
# thickness of capturer layer on the Y surface
bottom-scinblock.n-capt.y-thickness = 300 micrometer
# NEUDET CHAMBER
# global X size
chamber.width = 1.2 m
# global Y size
chamber.length = 1.2 m
# global Z size
chamber.thickness = 1.2 m
SC
Layer of
N-capturer
(Gd,Cd,...)
XY-view
103 MC-simulations
106 experimental tests
As a result:
conception
of the spectrometer

## Slide 13
S3
S-cube
Segmental solid plastic scintillator (2500 cells)
Sensitive
volume=1 m3
Cu (carriage frames =
-shield)
Pb
(-shield)
CH2 + B
(n-shield)
Plast. scnt.
(µ-shield)
DANSS

## Slide 14: Basic element – - scintillator cell (“strip” )
Gd-containing
light-reflecting
coating
Polystyrene-based scintillator
3 wave-length shifting (WLS) fibers Ø1.2 mm

## Slide 15
Blind end of each WLS-fiber is coated (chemically) with light reflector

## Slide 16
Modular structure of the detector
A number of strips are combined into intercrossing X- and Y-modules.

## Slide 17
Prototype: 2 parallel modules (no Gd-coating)

## Slide 18: Light collection
One PMT per Module (25-50 strips):
measure total energy of the photon burst
produce “hard trigger”
Individual photo-diod (SiPM or MPPC) per each strip:
space distribution of the photon burst
R 50W
hn
pixel
U
Al
base

## Slide 19
MPPC (Russia)
PMT
(Japan)
PMT+HV
(Japan)

## Slide 20
MPPC preamplifiers

## Slide 21
Flash ADC etc.

## Slide 22
ADC gate
ADC input

Light sensor
(H6780, etc.)
&
pedestal
Single photo-electron peak
Cosmic
muons
ADC-channels
Typical
energy
spectrum
Test bench for strips,
WLS-fibers and photo sensors

## Slide 24
Monte Carlo simulations
Example:
Space distribution of the energy deposit after the 157Gd(n,) reaction

## Slide 25: Start the real creation!
End of 2009:
Enough of R&D.

## Slide 26
Carriage frames

## Slide 30
MPPC
Twisted pair (to PA)
2 fibes to PMT

## Slide 31
Mounting table (with Cu bottom shielding)

## Slide 32
Mounting of the first section

## Slide 38: The section #0 was dismounted and sent to Moscow (our ITEP-members of the team are playing with it now). After some corrections we have started production of the sections #1, #2, etc.

## Slide 39
The GEMMA-1 site:
Reactor unit #2 of the
“Kalinin” Nuclear Power Plant
(400 km North from Moscow)
Technological room
just under reactor
14 m only!
2.71013 /cm2/s
Overburden
(reactor, building, shielding, etc.):
~70 m of W.E.

## Slide 40: GEMMA background conditions
-rays were measu- red with Ge detector. The main sources are: 137Cs , 60Co, 134Cs.
Neutron background was measured with 3He counters, i.e., thermal neutrons were counted. Their flux at the facility site turned out to be 30 times lower than in the outside laboratory room.
Charged component of the cosmic radiation (muons) was measu-red to be 5 times lower than outside.

## Slide 41
КАЭС
s
i
t
e
a
v
a
i
l
a
b
l
e
To be started on Sept. 2011
14 →10 m
5∙1013 /cm2/s

## Slide 43
Lifting
mechanism
GEMMA-2

## Slide 45
Could we make the same for the DANSS

## Slide 47
Lifting mechanism
4.1 m

## Slide 48: Important features (resp. to conventional liquid scint.)
Handling is much safer (not caustic, spontaneously igniting, volatile or solvent) → no restrictions to move the detector very close to the reactor core → higher neutrino flux → better sensitivity.
High segmentation (2500 cells) → space information → better IBD-signature → stronger BCKG suppression.
PS is not doped with Gd, but interlayed with it → better quality and stability of the scintillator.
WLS-fibers improve homogeneity of light-collection → better energy resolution.
Each cell in a module is looked through with both individual MPPC (high QE, but bad noise and range) and common PMT (lower QE, but better range and stability) → coincidence mode and combination of PMT and MPPC advantages.
Sectional structure → possibility of “partial” operation, renewal and upgrade.
Use of lifting mechanism → measurements at different distance → more reliable data interpretation.

## Slide 49: Expected parameters:
Sensitive volume: 1 m3
Composition: 5 sections (1m × 1m × 0.2m)
or 10 sections (1m × 1m × 0.1m)
of (5X + 5Y) modules = 2500 scint. strips { 1 module = 5 × 10 = 50 strips }
IBD detection efficiency: 74%
Count rate: 9200 IBD-events per day
Background: 40-50 events per day
Due date: section №0 – Feb 2010
sections №1-3 – 2011 №4-5 – 2012